## Slide 1: RTL Design Methodology
Sec 6.2-6.5
Lecture 05

## Slide 2: What is RTL design?
a quick overview

## Slide 3: What is a register
a variable in a chip
an n-bit storage device
  triggered by clock
  D flip-flop is an 1-bit register
may with various control signals (load, shift, counting, etc.)
4
4
D
Q
clock
D
Q
in
out
clk

## Slide 4: What is RTL design (1) (What’s the clock for?)
Answer: to make the circuit doing step-by-step computation
  clock signal is fed to all registers of the circuit
  to let a sequential circuit performs its task in step-by-step manner
    one step: a micro-operation (Section 6-3)
  forms a sequence of state change on flip flops
    imagine the flip flops as variables for programming
A
B
X
0010
0101
1
0111
1000
1
1001
1010
0
1111
0000
0
1100
0011
0
time
clock
registers
input
sequence of state change
clock
Figure 5-1
registers A, B, C, …
A=B+C

## Slide 5: What is RTL design (2)
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 6: RTL Design Methodology
an overview

## Slide 7: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 8: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
Hey you, do A=B+C
A=B+C, where A, B, C are registers

## Slide 9: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
I got overflow from A=B+C, sir

## Slide 10: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 11: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 12: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 13: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)

## Slide 14: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 4)
  data path: micro-operation to circuit (Sec. 6.3 – 6.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 15: Micro Operations

## Slide 16: What is RTL design (1) (What’s the clock for?)
Answer: to make the circuit doing step-by-step computation
  clock signal is fed to all registers of the circuit
  to let a sequential circuit performs its task in step-by-step manner
    one step: a micro-operation (Section 7-3)
  forms a sequence of state change on flip flops
    imagine the flip flops as variables for programming
A
B
X
0010
0101
1
0111
1000
1
1001
1010
0
1111
0000
0
1100
0011
0
time
clock
registers
input
clock
Figure 5-1
registers A, B, C, …
A=B+C

## Slide 17: Examples
a simple transfer
conditional transfer
a simple arithmetic
conditional arithmetic

## Slide 18: Example 1
R1
R2
0010
x
0111
1001
1111
1100
time
clock
registers
0010
0111
1001
1111

## Slide 19: Example 2
R1
R2
0010
x
0111
1001
time
clock
registers
0010
0010
K1
1
0
0
register with load enable (Figure 6-2)

## Slide 20: Example 3
+
R1
R2
R0
R1
R2
10
5
2
8
time
clock
registers
7
2
R0
X
15
9
an adder

## Slide 21: Example 4

## Slide 22: RTL Design Example
Q=A+B+C+D with only one adder

## Slide 23: The Problem
use only one adder to compute Q=A+B+C+D
  start computing when “START” button pressed
  hold the result in Q and inform by LED “FINISH”
Accumulator
n
A
n
B
n
C
n
D
START
n
Q
FINISH

## Slide 24: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 25: The hardware algorithm

## Slide 26: Steps to do Q=A+B+C+D
Notes:
  each state holds for one cycle
  one step performs a micro-operation with combinational circuit
STOP
Step 0
Step 1
Step 2
Step 3
the four steps to
compute Q=A+B+C+D

## Slide 27: Behavior spec of the datapath

## Slide 28: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 29: Behavior of the data path
STOP
Step 0
Step 1
Step 2
Step 3
Q
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]

## Slide 30: Behavior of the data path
STOP
Step 0
Step 1
Step 2
Step 3
Q
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
all micro-operations in the algorithm

## Slide 31: Behavior of the data path
STOP
Step 0
Step 1
Step 2
Step 3
Q
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
3-bit signal for the command
S

## Slide 32: Behavior spec of the control unit
the state diagram

## Slide 33: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 34: Behavior of the control unit
just send corresponding signals for required operation
STOP
Step 0
Step 1
Step 2
Step 3
STOP
Step 0
Step 1
Step 2
Step 3
S=100
S=000
S=101
S=110
S=111

## Slide 35: Behavior spec
S[2:0]
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Q

## Slide 36: Circuit of the data path

## Slide 37: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 38: Circuit of the data path
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Adder
MUX
A
B
C
D
MUX
0
register Q
Load
S[1:0]
OR
S[1]
S[0]
S[2]

## Slide 39: Circuit of the data path
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Adder
MUX
A
B
C
D
MUX
0
register Q
Load
S[1:0]
OR
S[1]
S[0]
S[2]
0
holds the original value

## Slide 40: Circuit of the data path
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Adder
MUX
A
B
C
D
MUX
0
register Q
Load
S[1:0]
OR
S[1]
S[0]
S[2]
1
loads input from the adder

## Slide 41: Circuit of the data path
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Adder
MUX
A
B
C
D
MUX
0
register Q
Load
S[1:0]
OR
S[1]
S[0]
S[2]
1
0
0
0
00

## Slide 42: Circuit of the data path
0
X
X
1
0
0
1
0
1
1
1
0
1
1
1
S[2:0]
Adder
MUX
A
B
C
D
MUX
0
register Q
Load
S[1:0]
OR
S[1]
S[0]
S[2]
1
0
1
1
01

## Slide 43: Timing diagram of the data path
time
A
B
C
D
S
Q
1000
0100
0010
0001
100
101
110
111
000
xxxx
1000
1100
1110
1111

## Slide 44: Put it all together: How the data path works

## Slide 45: Put it all together: How the datap ath works
1
00
00

## Slide 46: Put it all together: How the datap ath works
1
01
01

## Slide 47: Circuit of the control unit

## Slide 48: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 49: State assignment
3 D flip-flops
the state value equals the control!
STOP
Step 0
Step 1
Step 2
Step 3
S=100
S=000
S=101
S=110
S=111
000
100
101
110
111
S=100
S=000
S=101
S=110
S=111

## Slide 50: Standard method to realize a state diagram
0XX
0
000
0XX
1
100
100
X
101
101
X
110
110
X
111
111
X
000
S[2:0]
START
D[2:0]
D flip-flops
S[2:0]
combinational
circuit
START
D[2:0]

## Slide 51: Some tricks to implement the control unit
use a counter for S[1:0]
  be careful for the logic to set S[2]
use a counter for the whole state diagram
  be careful on the count-enable control
011
100
101
110
111
S=100
S=011
S=101
S=110
S=111

## Slide 52: Timing diagram of the control unit
time
A
B
C
D
S
state
1000
0100
0010
0001
Step 0
Step 1
Step 2
Step 3
Stop
100
101
110
111
000

## Slide 53: Timing diagram of the control unit

## Slide 54: How the hardware Q=A+B+C+D works
put it all together

## Slide 55: The whole circuit

## Slide 56: Timing diagram of the circuit
time
A
B
C
D
S
Q
state
1000
0100
0010
0001
Step 0
Step 1
Step 2
Step 3
Stop
100
101
110
111
000
xxxx
1000
1100
1110
1111

## Slide 57: Timing diagram of the circuit
time
A
B
C
D
S
Q
state
1000
0100
0010
0001
Step 0
Step 1
Step 2
Step 3
Stop
100
101
110
111
000
xxxx
1000
1100
1110
1111
state sequence of the control unit

## Slide 58: Timing diagram of the circuit
time
A
B
C
D
S
Q
state
1000
0100
0010
0001
Step 0
Step 1
Step 2
Step 3
Stop
100
101
110
111
000
xxxx
1000
1100
1110
1111
operations of the data path
control signal affects the content of Q at the next cycle

## Slide 59: Exercise
R=|A-B| with only one adder

## Slide 60: Problem Description
Design a hardware to compute R=|A-B| using only one adder
Write down the following:
  State transition diagram with micro-operations annotated
  Circuit of the data path
  Circuit of the control unit (specifying the truth-table of combinatorial part only)
R=|A-B|
n
A
n
B
n
R
clock
start

## Slide 61: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: design the data path
  micro-operations
  the circuit data path
Step 3: design the control unit
  finite state machine
  sequential circuit realization

## Slide 62: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start

## Slide 63: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
no operation, keep value of R

## Slide 64: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
R=A-B

## Slide 65: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
check if R<0 or not
R>=0
R<0

## Slide 66: Algorithm to compute R=|A-B|
R = A+(~B)+1;
if (R[n-1]==1)
R = (~R)+1;
S0
S1
S2
S3
start
R=-R

## Slide 67: The data path to compute R=|A-B|

## Slide 68: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: design the data path
  micro-operations
  the circuit data path
Step 3: design the control unit
  finite state machine
  sequential circuit realization

## Slide 69: The data path
make sure that all micro-operations can be realized!
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0

## Slide 70: Exercise 1
write down the control signal value to realize each of the micro-operations
  R(t+1)=A+(~B)+1
  R(t+1)=(~R(t))+1
  R(t+1)=(~R(t))
you may give your own MUX encoding as you like
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0

## Slide 71: Control Signal
Realize R(t+1)=~R(t)+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
Enable
MUX
1
0
1
0
0

## Slide 72: Control Signal
Realize R(t+1)=A+(~B)+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
Enable
MUX
1
0
1
1
1

## Slide 73: Control Signal
Realize R(t+1)=R(t)
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
not loading the input
MUX
1
0
0
X
X
outcome of this part is don’t-care

## Slide 74: The control unit

## Slide 75: What’s the control unit for
hardware to send out control signals
to ask the data path to perform required micro-operations for each cycle
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
R[n-1]

## Slide 76: Behavior specification of the control unit
write down the control signals for each state
  to perform required operations
S0
S1
S2
S3
start

## Slide 77: Behavior specification of the circuit
Check the match between control signals and data path
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
S0
S1
S2
S3
start

## Slide 78: How to realize the control unit
standard method to realize a finite-state machine (Chap. 5)
D flip-flops
S[1:0]
combinational
circuit
start
{L, S1, S0}
S0
S1
S2
S3
start

## Slide 79: The timing diagram
Can you image how the circuit works?

## Slide 80: Problem
Draw the timing diagram until the outcome R finished
A
3
B
8
start
1
0
(L, S1, S0)
state
S0
???
???
R[n-1]
???
R
???

## Slide 81: Rule of Thumb
Combinational Circuit: generate outputs at the same cycle to inputs
D Flip-Flop: A(t+1) = DA(t)
  state changes at the next cycle

## Slide 82: Timing of the control unit
control unit appears at the same cycle to the state
time
clock
state
(L,S1,S0)
S1
(1,1,1)
the same cycle
by combinational circuit

## Slide 83: Timing of the control unit
state changes at the next cycle
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2

## Slide 84: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 85: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x
combinational circuit
1
1
follows the
control signal

## Slide 86: Timing of the data path
Computation at cycle t follows the control signals sent at cycle t
But the result appears on the register at cycle t+1
MUX
A
0
MUX
B
R
NOT
adder
Cin
1
register R
load
L
S1
S0
X
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x
1
stored at the
next cycle

## Slide 87: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 88: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 89: Timing of the whole circuit
realize the hardware algorithm:
  do the required computation at each cycle
  and store the result at the next cycle
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 90: Timing of the whole circuit
state transition following the state diagram
S0
S1
S2
S3
start
time
clock
state
(L,S1,S0)
S1
(1,1,1)
S2
X
A+~B+1
register R
A+~B+1
x

## Slide 91: Timing diagram of an working example
You just have to look at the hardware algorithm
A
3
B
8
start
1
0
(L, S1, S0)
state
S0
R[n-1]
R
(0,X,X)
x
x
S1
(1,1,1)
x
x
S2
-5
(0,X,X)
1
S3
(1,0,0)
-5
1
5
0
S0
(0,X,X)