## Slide 1: Basic Arithmetic Circuits
Recall: add/sub of digital circuit course
Appendix of Lecture 05

## Slide 2: Outline
Adder Design
Signed Number Representation
Exercise: |A-B|
  C-code
  hardware design

## Slide 3: Addition

## Slide 4: How a computer performs binary addition
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S

## Slide 5: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 6: How a computer performs binary addition
Step 1: addition for bit 0
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
Carry C[1]
Sum S[0]

## Slide 7: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}

## Slide 8: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1

## Slide 9: How a computer performs binary addition
Step 2: addition for bit 1 with carry
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0
1
0
Carry C[2]
Sum S[1]

## Slide 10: How a computer performs binary addition
repeat the procedure and we get the result
for each bit i=0 to N-1 do {
{C[i+1], S[i]} = A[i]+B[i]+C[i]
}
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1
So, what’s the basic cell for the addition?

## Slide 11: Full Adder: the basic component for an adder
a combinational circuit doing the following truth table
to perform addition for a bit i
FA
X
Y
S
Cin
Cout
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Cin
Cout
S
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
0
1

## Slide 12: Full Adder: the basic component for an adder
a combinational circuit doing the following truth table
to perform addition for a bit i
FA
X
Y
S
Cin
Cout
0
0
0
0
0
0
0
1
0
1
0
1
0
0
1
0
1
1
1
0
1
0
0
0
1
1
0
1
1
0
1
1
0
1
0
1
1
1
1
1
X
Y
Cin
Cout
S
0 1 1 0
0 0 1 1
+)
A
B
S
1
0
0
1
0
1
1
1
0

## Slide 13: Full-adder implementation

## Slide 14: Ripple-Carry Adder
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1

## Slide 15: Ripple-Carry Adder
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1

## Slide 16: Ripple-Carry Adder
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1

## Slide 17: Signed number and subtraction

## Slide 18: Signed number representation (2’s complement)
the general format
  4-bit signed number
  representing -8 ~ 7
sign bit

## Slide 19: Signed number representation (2’s complement)
Example: representing positive number +5
0
1
0
1
sign bit
positive number

## Slide 20: Signed number representation (2’s complement)
Example: representing negative number -5
Rule:
1
0
1
1
sign bit
negative number
0
1
0
1
A=+5
1
0
1
0
1
0
1
1

## Slide 21: Signed number representation (2’s complement)
Property:
0
1
0
1
sign bit
1
0
1
1
A=-5
0
1
0
0
0
1
0
1
+5

## Slide 22: How to do subtraction
use adder with 2’s complement encoding

## Slide 23: Method to do subtraction
Rule:
Example: A=5, B=3
0
0
1
1
B=3
1
1
0
0
1
1
0
1
0
1
0
1
A=5
1
1
0
1
-B=-3
+)
0
0
1
0
1
A-B=2

## Slide 24: Method to do subtraction
Rule:
Example: A=3, B=5
0
1
0
1
B=5
1
0
1
0
1
0
1
1
0
0
1
1
A=3
1
0
1
1
-B=-5
+)
1
1
1
0
0
A-B=-2

## Slide 25: Rule of thumb
Key Properties:
Apply whenever positive or negative
Why?
  lots of mathematics
  I will talk about this more in “computer arithmetic” course

## Slide 26: In-Class Exercise
to help you learn the above concept

## Slide 27: In-Class Exercise
(open book, may discuss with others)
Q1: write a C-code to calculate |A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available
Q2: design hardware for both addition and subtraction
adder/subtractor
S
B
n
A
n
n
G

## Slide 28: Method to take absolute value
|A-B| in C

## Slide 29: Problem
write a C-code to calculate |A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available

## Slide 30: The Solution
write a C-code to calculate Q=|A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available
R = A+(~B)+1;
Q = (R & 0x80000000)? (~R)+1: R;

## Slide 31: The Solution
write a C-code to calculate Q=|A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available
R = A+(~B)+1;
Q = (R & 0x80000000)? (~R)+1: R;

## Slide 32: The Solution
write a C-code to calculate Q=|A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available
R = A+(~B)+1;
Q = (R & 0x80000000)? (~R)+1: R;
check if R31=1 or 0

## Slide 33: The Solution
write a C-code to calculate Q=|A-B|
  you cannot use the following operators: -, >, <, >=, <=
  only add(+) and bit-wise logical operators available
R = A+(~B)+1;
Q = (R & 0x80000000)? (~R)+1: R;

## Slide 34: Adder/Subtractor Design

## Slide 35: Goal
Design hardware for both addition and subtraction
adder/subtractor
S
B
n
A
n
n
G

## Slide 36: The Design
adder
MUX
n
n
~B
n
B
n
A
S
Cin
S
n
G

## Slide 37: Recall: the adder design
FA
FA
FA
FA
FA
…
A[0]
B[0]
A[1]
B[1]
A[2]
B[2]
A[n-2]
B[n-2]
A[n-1]
B[n-1]
S[0]
S[1]
S[2]
S[n-2]
S[n-1]
Cin
Cout
Adder
n
A
n
B
n
S
Cin
Cout
always @(*)
{Cout, S} = A+B+Cin;
0 1 1 0
0 0 1 1
+)
A
B
S
1 0 0 1
Carry-in
Carry-in

## Slide 38: The Design
adder
MUX
n
n
~B
n
B
n
A
S
Cin
S
n
G
0
0
G=A+B+0

## Slide 39: The Design
adder
MUX
n
n
~B
n
B
n
A
S
Cin
S
n
G
1
1
G=A+(~B)+1

## Slide 40: Summary
Most important properties of 2’s complement encoding:
sign bit