## Slide 1: RTL Coding with Verilog
Lab 07

## Slide 2: Purpose of this lab
to learn Verilog grammar and synthesizable coding style
setup of your imagination of transform a hardware diagram to Verilog
+
B
C
A
clk
register
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end

## Slide 3: Your Tasks (70% basics)
Ex1: block design in structural description
Ex2: design a combinational circuit by specifying Boolean equations
Ex 3: circuit design from truth table (behavior description)
Ex 4: realizing a state-diagram with behavior description (if-then-else)

## Slide 4: Your Task: (+20% bonus) Problem: Max-Min Circuit
Design a circuit to
  find the minimum and maximum number
  from a series of 4 input numbers
  output max and min in series
Design Constraint:
  only two n-bit registers are allowed to store the value for computation
min-max
circuit
start
n
X
n
Y
start
X
Y
1
1000
1100
0010
0001
0
1100
0001
XXXX
XXXX
time

## Slide 5: Block Design with Structural Description
Exercise 01

## Slide 6: Exercise 01
Write a Verilog module for this accumulator circuit
provided that the following sub-modules are given
  adder
  MUX
  register with load enable
Register R
Load
MUX
adder
0
8
A
in1
in0
D
Q
8
8
8
L
S

## Slide 7: Combinational Circuit Design with Boolean Equation
Exercise 02

## Slide 8: Exercise 02
Design the circuit with “assign” statements
  write the Boolean equations

## Slide 9: Circuit design with truth table
Exercise 03

## Slide 10: Exercise 03
design the circuit with behavior description
  specify the truth table/state-transition diagram

## Slide 11: Realizing state-diagram with behavior description
Exercise 04

## Slide 12: Exercise 04
Design a sequential circuit to realize the state diagram
  use behavior description
  use if-then-else and case statements
A
B
C
D

## Slide 13: Requirements to your reports

## Slide 14: Requirements to your Pre-Lab Reports
Verilog coding
synthesized circuit
  please map each part of your code to the synthesized circuit
simulation waveform for typical cases