## Slide 1: Synthesizable Verilog Coding
for RTL design
Lecture 07

## Slide 2: Course Material
[Thomas] Thomas &Moorby, The Verilog Hardware Description Language, 5/e, Kluware Academic, 2008
[Uyemura] J. P. Uyemura, Introduction to VLSI Circuits and Systems, John Wiley & Sons, 2002
Find your favorite Verilog book and read by yourself!

## Slide 3: Course package of this lecture
power point slides:
  lec07-verilog.pptx: concepts of Verilog coding
  lab07-verilog.ppt:x exercises for this lab
  lec07a-abs_diff: RTL design example R=|A-B|
Verilog source code:
  sub-dir components: for Ex01
  sub-dir abs_diff: the demo code of R=|A-B|
  sub-dir synthesis_demo: a demo code to show you Verilog->HW synthesis

## Slide 4: Let’s start from RTL design

## Slide 5: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 6: Goal of this lecture
let you do RTL design using Verilog
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
K: A=B+C
(if (K==1) then A=B+C;)
by EDA tool

## Slide 7: How to make a (digital) chip

## Slide 8: VLSI Design Flow in SoC Era
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 9: The basic device to build a chip: MOS transistor
G
D
S
X
X=0
X=1
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 10: Physical Layout
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 11: Physical layout of a chip
The image you find in fully-custom design

## Slide 12: Gate-level to Circuit-level Transform
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout

## Slide 13: RTL to Gate-level transform
ESL design
(Electronic System Level)
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout
reg A, B, C, D, E;
always @(*)
E = A&B | C&D;

## Slide 14: State-of-art chip design
RTL design
(Register Transfer Level)
gate-level design
circuit-level design
(transistor-level)
physical layout
always @(posedge clk)
A <= B+C;
automatically
processed by EDA
tools

## Slide 15: Still some comments before we begin

## Slide 16: Common error of beginners
non-synthesizable coding style
  a wrong code may result in correct simulation wave-form/FPGA outcome
synthesizable but without concrete imagine on hardware generated
  long path delay
  extremely large chip area

## Slide 17: Caution
(adopted from CIC technical report)

## Slide 18: Correct method of doing RTL coding
Step 1: draw the block diagram of your hardware
  be aware of combinational and sequential circuit
Step 2: translate each block into Verilog/VHDL code
  follow fixed coding style
always have a hardware block diagram in your minds!

## Slide 19: Suggestion to beginners
do “synthesis” for each small piece of your code
  synthesis means: translate a higher level design to a lower level design (e.g. RTL=> gate-level)
use “Tools->Net List Viewer -> RTL view” of Quartus II

## Slide 20: Now we begin to talk about Verilog coding

## Slide 21: Verilog coding
structural description
  describe the hardware directly
behavior description
  the “register transfer” rules
  most of beginners error
input A [3:0];
input B [3:0];
input clock;
reg S [3:0];
always @(posedge clock)
S <= #1 A+B;

## Slide 22: Structural description (1)
describing a hardware with block diagram in minds

## Slide 23: What is structural description
describing a hardware with detailed block diagram in minds

## Slide 24: A “module”
the basic unit for Verilog hardware design is a “module”
  the hardware you designed is a module
  you may have sub-modules in your design
structural description to describe the hardware architecture of a module:
  Step 1: module declaration with input/output specifications
  Step 2: instance sub-modules
  Step 3: declare wires and make connections

## Slide 25: Example of structural description

## Slide 26: Example of structural description
module declaration
the module you designed

## Slide 27: Example of structural description
input/output specification

## Slide 28: Example of structural description

## Slide 29: Example of structural description

## Slide 30: A “module”
the basic unit for Verilog hardware design is a “module”
  the hardware you designed is a module
  you may have sub-modules in your design
structural description to describe the hardware architecture of a module:
  Step 1: module declaration with input/output specifications
  Step 2: instance sub-modules
  Step 3: declare wires and make connections

## Slide 31: Instance Sub-Modules

## Slide 32: Instance Sub-Modules
type of this sub-module

## Slide 33: Instance Sub-Modules
name of this block
(you can give any name as you want)

## Slide 34: A sub-module with detailed design

## Slide 35: A “module”
the basic unit for Verilog hardware design is a “module”
  the hardware you designed is a module
  you may have sub-modules in your design
structural description to describe the hardware architecture of a module:
  Step 1: module declaration with input/output specifications
  Step 2: instance sub-modules
  Step 3: declare wires and make connections

## Slide 36: Declare wires

## Slide 37: Connecting ports of modules

## Slide 38: Lab Exercise
Write a Verilog module for this accumulator circuit
provided that the following sub-modules are given
  adder
  MUX
  register with load enable
Register R
Load
MUX
adder
0
8
A
in1
in0
D
Q
8
8
8
L
S

## Slide 39: Caution
always use “wire” to declare signals in structural description
no “always @(…)” in structural description

## Slide 40: Structural Description (2)
describe the hardware with Boolean/arithmetic equations

## Slide 41: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)

## Slide 42: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
E
module my_circuit (A, B, C, E);
input A;
input B;
input C;
output E;
wire D;
assign D = A&B;
assign E = C | D;
endmodule
the same operators to C/C++

## Slide 43: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
E
module my_circuit (A, B, C, E);
input A;
input B;
input C;
output E;
assign E = (A&B)|C;
endmodule
you may write a longer equation

## Slide 44: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
adder
8
8
8
A
B
C
module my_circuit (A, B, C);
input [7:0] A;
input [7:0] B;
output [7:0] C;
assign C = A+B;
endmodule
arithmetic equation in C

## Slide 45: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
module my_circuit (A, B, C, E);
input [7:0] A;
input [7:0] B;
input [7:0] C;
output [7:0] E;
wire [7:0] D;
assign D = A+B;
assign E = C+D;
endmodule
adder
8
8
8
A
B
C
adder
8
8
E
D

## Slide 46: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
module my_circuit (A, B, C, E);
input [7:0] A;
input [7:0] B;
input [7:0] C;
output [7:0] E;
wire [7:0] D;
assign E = C+D;
assign D = A+B;
endmodule
adder
8
8
8
A
B
C
adder
8
8
E
D
re-order yields the same result

## Slide 47: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
module my_circuit (A, B, C, E);
input [7:0] A;
input [7:0] B;
input [7:0] C;
output [7:0] E;
assign E = A+B+C;
endmodule
adder
8
8
8
A
B
C
adder
8
8
E
D

## Slide 48: The “assign” statement
the “assign” a wire as driven by some combinational circuit
Example 1: the Boolean equation
Example 2: the arithmetic equation
Example 3: the multiplexer (MUX)
module MUX (A, B, S, C);
input [7:0] A;
input [7:0] B;
input S;
output [7:0] C;
assign C = (S)? A: B;
endmodule
MUX
8
8
8
A
B
S
C
C-style expression

## Slide 49: Rule of thumb to use “assign”
describe a combinational circuit with Boolean or arithmetic equations
  an equation from inputs to outputs
  the same operators/expressions to C/C++
combinational
circuit
…
A
B
C
D

## Slide 50: Lab Exercise
Design the circuit with “assign” statements
  write the Boolean equations

## Slide 51: Behavior description

## Slide 52: General Semantics of Behavior Description
specify the rules for event-driven simulation
Remark: Verilog is originally for hardware simulation, not for hardware synthesis
hardware to be
simulated
A
B
C
D
E
reg D, E; //declare variables but
//not necessary synthesis registers
always @(event_list) begin
…
// C code to compute D and E from A, B, C
…
end

## Slide 53: Inferring combinational circuit with behavior description

## Slide 54: Inferring combinational circuit
general coding style:
  always @(list of all input signals)
  always @(*)
  use blocking assignment “=“
    do not use “<= “
  you have to enumerate all cases to determine the output value

## Slide 55: Example: a combinational circuit
semantics from event-driven simulation
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
A
B
C
E
clock
0
1
1
0
0
1
time

## Slide 56: Example: a combinational circuit
semantics from event-driven simulation
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
A
B
C
E
clock
0
1
1
0
0
1
time
events to trigger the simulation

## Slide 57: Example: a combinational circuit
semantics from event-driven simulation
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
A
B
C
E
clock
0
1
1
0
0
1
time
C-like statements to simulate

## Slide 58: Example: a combinational circuit
semantics from event-driven simulation
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
A
B
C
E
clock
0
1
1
0
0
1
time
signal change causes the simulation
the simulated output value

## Slide 59: Example: a combinational circuit
semantics from event-driven simulation
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
A
B
C
E
clock
0
1
1
0
0
1
time
signal change not waiting for a clock

## Slide 60: Example: a combinational circuit
the synthesized circuit
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
E

## Slide 61: Example: a combinational circuit
the synthesized circuit
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule
E
declared as a register but not register synthesized

## Slide 62: More Examples of inferring combinational circuits
design by specifying the Boolean equations
design by specifying the truth table
inferring a data path with case statement
inferring a data path with if-then-else

## Slide 63: Example 1 (a)
design by specifying Boolean equations
E
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(A or B or C) begin
E = (A&B)|C;
end
endmodule

## Slide 64: Example 1 (b)
design by specifying Boolean equations
E
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(*) begin
E = (A&B)|C;
end
endmodule
simulation triggered by any change on input signals

## Slide 65: Example 1 (c)
design by specifying Boolean equations
E
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg D;
reg E;
always @(*) begin
D = A&B;
end
always @(*) begin
E = D|C;
end
endmodule

## Slide 66: Example 1 (d)
design by specifying Boolean equations
E
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg D;
reg E;
always @(*) begin
E = D|C;
end
always @(*) begin
D = A&B;
end
endmodule
exchange yields the same result

## Slide 67: More Examples of inferring combinational circuits
design by specifying the Boolean equations
design by specifying the truth table
inferring a data path with case statement
inferring a data path with if-then-else

## Slide 68: Example 2
inferring combinational circuit by specifying the truth table
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(*) begin
case ({A, B, C})
3’b000: E = 1’b0;
3’b001: E = 1’b1;
3’b010: E = 1’b0;
3’b011: E = 1’b1;
3’b100: E = 1’b0;
3’b101: E = 1’b1;
3’b110: E = 1’b1;
3’b111: E = 1’b1;
endcase
end
endmodule
E

## Slide 69: Example 2
inferring combinational circuit by specifying the truth table
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(*) begin
case ({A, B, C})
3’b000: E = 1’b0;
3’b001: E = 1’b1;
3’b010: E = 1’b0;
3’b011: E = 1’b1;
3’b100: E = 1’b0;
3’b101: E = 1’b1;
3’b110: E = 1’b1;
3’b111: E = 1’b1;
endcase
end
endmodule
E
the truth table

## Slide 70: Constant Representation
binary number:
  [width]’bnumber
  Example 1: ‘b101
  Example 2: 3’b101
hexdecimal number
  [width]’hnumber
  Example 1: ‘h09a2
  Example 2: 16’h09a2
decimal:
  Example: 1234
  Example: ‘d1234
  Example: 32’d1234

## Slide 71: Example 2
inferring combinational circuit by specifying the truth table
module demo_circuit (A, B, C, E);
input A, B, C;
output E;
reg E;
always @(*) begin
case ({A, B, C})
3’b000: E = 1’b0;
3’b001: E = 1’b1;
3’b010: E = 1’b0;
3’b011: E = 1’b1;
3’b100: E = 1’b0;
3’b101: E = 1’b1;
3’b110: E = 1’b1;
3’b111: E = 1’b1;
endcase
end
endmodule
E
E = 1 if {A,B,C}==001

## Slide 72: More Examples of inferring combinational circuits
design by specifying the Boolean equations
design by specifying the truth table
inferring a data path with case statement
inferring a data path with if-then-else

## Slide 73: Example: combinational circuit

## Slide 74: Example: combinational circuit
register is not a register!

## Slide 75: Example: combinational circuit
C-like code to compute output from inputs

## Slide 76: Example: combinational circuit
specify a don’t-care

## Slide 77: More Examples of inferring combinational circuits
design by specifying the Boolean equations
design by specifying the truth table
inferring a data path with case statement
inferring a data path with if-then-else

## Slide 78: Example: combinational circuit
if-then-else rules also work!

## Slide 79: Example: combinational circuit
This line is necessary to enforce
a combinational circuit

## Slide 80: Example: combinational circuit
Verilog 2001 standard:
depends on all input signals

## Slide 81: Inferring sequential circuit with behavior description

## Slide 82: The general scheme
for sequential circuit
  only simulate when clock triggered
hardware to be
simulated
A
B
C
D
E
always @(posedge clk) begin
…
// C code to compute D and E
…
end
clk

## Slide 83: Inferring sequential circuit
coding style:
  always @(posedge clk)
  use non-blocking assignment “<=“

## Slide 84: Example 1:
parallel D-FFs triggered by clock
time
rin
acc_reg
1010
0110
1010
0110
clock
rin
acc_reg

## Slide 85: Example 1
parallel D-FFs triggered by clock
simulation triggered by clock
time
rin
acc_reg
1010
0110
1010
0110
clock
rin
acc_reg

## Slide 86: Example 1
parallel D-FFs triggered by clock
Caution: You have to use non-blocking assignment
to generate registers!
time
rin
acc_reg
1010
0110
1010
0110
clock
rin
acc_reg

## Slide 87: Example 2: sequential circuit
with combinational circuit for computation

## Slide 88: Example 3: realizing finite-state machine
realize the finite-state machine with behavior description
0
1
X=0
X=1
T=1
T=0
reg S;
always @(posedge clock) begin
case (S)
1’b0:
begin
if (X==0)
S <= 1’b0;
else
S <= 1’b1;
end
1’b1: S <= (T)? 1’b1: 1’b0;
endcase
end

## Slide 89
I believe that most of you are confused with
  combinational circuit vs.
  sequential circuit

## Slide 90: Example: the adder
combinational vs. sequential circuit

## Slide 91: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end

## Slide 92: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
+
B
C
A
+
B
C
A
clk
register

## Slide 93: What’s the difference?
reg [3:0] A, B, C;
always @(*) begin
A = B+C;
end
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
10
5
15
1
2
3
5
7
12
B
C
A
clk
10
5
15
1
2
3
5
7
12
B
C
A
clk

## Slide 94: Caution on behavior description
Be aware of which part is combinational circuit and which part is sequential circuit
use fixed coding style for
  combinational circuit
  sequential circuit
Do not try other coding styles!

## Slide 95: Rule of thumb
declaration on “variables”
  structural description: wire
  behavior description: reg

## Slide 96: Rule of thumb for behavior description
for combinational circuit:
  always @(all signals used)
  always @(*)
  use “=“ (blocking assignment)
for sequential circuit
  always @(posedge clock)
  use “<=“ (non-blocking assignment)

## Slide 97: Final Remarks
find a Verilog book for details
  we don’t have time to talk about Verilog coding in detail
If you don’t like Verilog, you can still keep on drawing block diagrams
  Verilog is not a must in this course

## Slide 98: The next lecture
we will go into Chap. 8
  “Computer Design Basics”
Recall “digital circuit” before the class
  adder design
  2’s complement
  how to do add/subtract