## Slide 1: Processor Data Path Design
Lecture 09

## Slide 2: Today’s Goal
guide you to design the data path of a processor
Figure 8-15: single-cycle CPU

## Slide 3: Generic CPU data path

## Slide 4: Recall: RTL design also applied for CPU
Step 0: define the “assembly instructions” of the CPU
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
Just apply the general
RTL design method!

## Slide 5: What is a CPU data path for?
a generic hardware to do any arithmetic operations
control
unit
CPU data path
control signals
R=|A-B|+(C-D)
design a
custom control

## Slide 6: Generic CPU data path

## Slide 7: Generic CPU data path
register file
  the internal storage (memory) within a CPU
  contains a set of registers R0, R1, R2, …
  totally 8 registers in this sample design

## Slide 8: Generic CPU data path
function unit
  to perform arithmetic operations
  Example: add, subtraction, logical AND/OR/NOT,etc
  any C/C++ operators
    +, -, *, /, %
    &, |, ~, ^
    <<, >>

## Slide 9: Generic CPU data path
in our CPU design example
Figure 8-1

## Slide 10: How a CPU works?
from hardware design perspective
the data path:

## Slide 11: How a CPU works?
registers to store variables
registers

## Slide 12: How a CPU works?
function units to perform computation
function units

## Slide 13: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 14: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 15: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 16: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 17: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 18: Outline of the detailed design
Part 1: function unit
Part 2: the register file

## Slide 19: CPU function unit design
Part A

## Slide 20: The design spec
Primary computation data
  two n-bit inputs A and B
  one n-bit output F
  doing operations F = A op B
operation controlled by 4-bit control signal FS
flag output {V,C,N,Z}

## Slide 21: The design spec
Primary computation data
  two n-bit inputs A and B
  one n-bit output F
  doing operations F = A op B
operation controlled by 4-bit control signal FS
flag output {V,C,N,Z}

## Slide 22: The design spec
Primary computation data
  two n-bit inputs A and B
  one n-bit output F
  doing operations F = A op B
operation controlled by 4-bit control signal FS
flag output {V,C,N,Z}

## Slide 23: The design spec
operation controlled by 4-bit control signal FS
  to do F= A op B

## Slide 24: The design spec
operation controlled by 4-bit control signal FS
  to do F= A op B
0010
F=A+B

## Slide 25: The design spec
Primary computation data
  two n-bit inputs A and B
  one n-bit output F
  doing operations F = A op B
operation controlled by 4-bit control signal FS
flag output {V,C,N,Z}

## Slide 26: Why these operations
to realize these assembly instructions

## Slide 27: Design of the Function Unit

## Slide 28: Implementation Strategy

## Slide 29: Implementation Strategy
The ALU operations I taught you last week

## Slide 30: Implementation Strategy
shift 1-bit operations
F=B>>1, F=B<<1
new

## Slide 31: The shifter design of our CPU

## Slide 32: Spec of the shifter
shifter
n
B
n
H
2
S

## Slide 33: Design of the shifter
Rules for a bit i
MUX

## Slide 34: Design of the shifter
Rules for a bit i
MUX

## Slide 35: Design of the shifter
Rules for a bit i
MUX

## Slide 36: Design of the shifter
Rules for a bit i
MUX

## Slide 37: Design of the shifter
the complete circuit
Rules for a bit i
Figure 9-8

## Slide 38: Verilog coding for the shifter
always @(*) begin
case (S)
2’b00: H = B;
2’b01: H = {1’b0, B[7:1]};
2’b10: H = {B[6:0], 1’b0};
2’b11: H = 8’hx;
endcase
end

## Slide 39: Put it all together
integration of a function unit

## Slide 40: Implementation Strategy

## Slide 41: Implementation Strategy
MUX to select for the outcome

## Slide 42: Implementation Strategy
use ALU

## Slide 43: Implementation Strategy
use the shifter

## Slide 44: How to generate the flag signals
still something left to the function unit

## Slide 45: Definitions of flags
flag output {V,C,N,Z} determined by ALU output F
  V: overflow
  C: carry out of the adder in ALU
  N: negative
  Z: zero
(check F[n-1])

## Slide 46: Why these flags
to realize if-then-else statements in a program

## Slide 47: Generating the overflow flag
70
80
+)
150
0100 0110
0101 0000
+)
1001 0110
1
0
-70
-80
+)
-150
1011 1010
1011 0000
+)
0110 1010
0
1

## Slide 48: Register File Design
Part B

## Slide 49: The Goal
Design the register file of a CPU
register file
Figure 9-1: CPU data path

## Slide 50: What is a register file

## Slide 51: What is a register file
a set of registers in CPU
  Recall Chap. 7: what is a register for digital system
  Recall Chap. 7: a register with load enable
storage elements to store computing data in a CPU

## Slide 52: How a CPU works?
registers to store variables
registers

## Slide 53: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 54: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 55: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 56: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 57: How a CPU works?
still follows von Neumann model
A = B+C;
load R1, B; //R1 = mem[B];
load R2, C; //R2 = mem[C];
add R3, R1, R2; //R3 = R1+R2;
store A, R3; //mem[A] = R3;
A
B
C
memory

## Slide 58: Spec of the register file we will design

## Slide 59: Spec of the register file
two read ports A and B
a read port is a set of input/output signals
to read data stored in the register file
read port A
read port B

## Slide 60: Spec of the register file
a read port (A)
register ID
to read
register data
read

## Slide 61: Spec of the register file
a read port (A)
register data
read
001
to read value of register R1
value of R1 flows out here

## Slide 62: Spec of the register file
a read port (B)
register data
read
010
to read value of register R2
value of R2 flows out here

## Slide 63: Spec of the register file
two reads may be performed in a cycle
R2
010
001
R1

## Slide 64: Spec of the register file
one write port
a set of input/output signals
to write data to a register
write port

## Slide 65: Spec of the register file
signals of the write port
write occurs only when Write=1
write enable

## Slide 66: Spec of the register file
specify which register to write
and the data to be written
register ID
to write
data to write to
a register

## Slide 67: Spec of the register file
Example of a write
011
12
1
time
clock
1
Write
011 (3)
D address
D data
12
R3
12
x
I want to write R3
R3=12

## Slide 68: Design of the register file

## Slide 69: Detailed design of register file
registers with load enable
(recall Chap. 6)

## Slide 70: Detailed design of register file
MUXs to implement read ports

## Slide 71: Detailed design of register file
read R1 from port A
001 to select R1

## Slide 72: Detailed design of register file
write port implementation

## Slide 73: Detailed design of register file
to write to R1
001 to write R1
1 to write enable

## Slide 74: Detailed design of register file
to write to R1
Q: why other registers won’t be written?
001 to write R1
1 to write enable
data to all registers

## Slide 75: The complete CPU data path
put it all together
Part C

## Slide 76: RTL design for the single-cycle CPU
Figure 8-15: the CPU

## Slide 77: RTL design for the single-cycle CPU
Figure 8-15: the CPU
control unit
data path

## Slide 78: RTL design for the single-cycle CPU
Figure 8-15: the CPU
control signals

## Slide 79: RTL design for the single-cycle CPU
Figure 8-15: the CPU
control signals
(routed to the data path)

## Slide 80
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
instruction
(e.g. ADD R1, R2, R3)
control signals generated
for an instruction

## Slide 81
Bus A
Bus B
Address out
Data out
MW
Data in
MUX B
1
0
MUX D
0
1
DATAPATH
RW
DA
AA
Constant
in
BA
MB
FS
V
C
N
Z
Function
unit
A
B
F
MD
Bus D
IR(2:0)
Data in
Address
Data
memory
Data out
Register
file
D
A
B
Instruction
memory
Address
Instruction
Zero fill
D
A
B
A
A
A
F
S
M
D
R
W
M
W
M
B
Instruction decoder
J
B
Extend
L
P
B
C
Branch
Control
V
C
N
Z
J
B
L
P
B
C
IR(8:6) || IR(2:0)
PC
CONTROL
instruction
(e.g. ADD R1, R2, R3)
control signals generated
for an instruction
to instruct the data path to perform
required operations for an instruction

## Slide 82: RTL design for the single-cycle CPU
Figure 8-15: the CPU
status signals sent back to the control unit
(for if-then-else)

## Slide 83: Example: doing R1=R2+R3

## Slide 84: How to realize the instruction
ADD R1, R2, R3 //R1=R2+R3
read R1 and R2 from register file
let the function unit do F=A+B (where A=R1 and B=R2)
write the result of function unit to R3 (R3=F)

## Slide 85: Realizing an instruction
R1=R2+R3
registers R1, R2, and R3 are here
R2
R3
adder is here
select R2
select R3
write enable
write R1
select B
do A+B
do A+B

## Slide 86: Read R2 and R3 from the register file
R1=R2+R3
registers R1, R2, and R3 are here
R2
R3
select R2
select R3
select B

## Slide 87: Function unit doing F=A+B
R1=R2+R3
R2
R3
adder is here
do A+B
select F

## Slide 88: Function unit doing F=A+B
R1=R2+R3
R2
R3
adder is here
do A+B
select F
0010

## Slide 89: Write-back: R1=F
R1=R2+R3
registers R1, R2, and R3 are here
write enable
write R1

## Slide 90: Remark
All these operations are done in one cycle
And the result appears at R1 on the next cycle
registers R1, R2, and R3 are here
R2
R3
adder is here
select R2
select R3
write enable
write R1
select B
do A+B
do A+B

## Slide 91: In-Class Exercise
R3=|R2-R1|

## Slide 92: Problem Description
use the CPU data path to do R3=|R2-R1|
  you have to do it with multiple cycles
write down
  finite state machine for control
  value of control signals for each state
control unit
you designed

## Slide 93: The finite state machine
STOP
R3 = R2-R1
if (R3<0) R3=~R3+1

## Slide 94: Realizing Micro-Operations
STOP
R2
R1
do F=R2-R1
registers R1, R2, and R3 are here

## Slide 95: Realizing Micro-Operations
STOP
R2
R1
do F=R2-R1
registers R1, R2, and R3 are here
N(t)=1 if R2(t)-R1(t)<0

## Slide 96: Realizing Micro-Operations
STOP
R2
R1
do F=R2-R1
registers R1, R2, and R3 are here
N(t)=1 if R2(t)-R1(t)<0
transition if R2-R1<0

## Slide 97: Realizing Micro-Operations
STOP
R2
R1
do F=R2-R1
registers R1, R2, and R3 are here
N(t)=1 if R2(t)-R1(t)<0
transition if R2-R1>=0

## Slide 98: Control signals
STOP
R2
R1
read R2
read R1
select Bdata
010
001
0

## Slide 99: Control signals
STOP
R2
R1
do A-B
select F
010
001
0
0101
0

## Slide 100: Control signals
STOP
R2
R1
write R3
010
001
0
0101
0
enable
1
011

## Slide 101: Control signals for R3=R2-R1
STOP
010
001
0
0101
0
1
011

## Slide 102: Control signals for all states
STOP
010
001
0
0101
0
1
011
011
XXX
0
1011
0
1
011
011
XXX
0
0001
0
1
011
XXX
XXX
X
XXXX
X
0
XXX