## Slide 1: Dash Watch
Example for RTL system design
(Section 6-10)
Lecture 06 (Part B)

## Slide 2: Recall: RTL design method
what Chap. 6 talks about

## Slide 3: What is RTL design (What’s the clock for?)
Answer: to make the circuit doing step-by-step computation
  clock signal is fed to all registers of the circuit
  to let a sequential circuit performs its task in step-by-step manner
    one step: a micro-operation (Section 7-3)
  forms a sequence of state change on flip flops
    imagine the flip flops as variables for programming
A
B
X
0010
0101
1
0111
1000
1
1001
1010
0
1111
0000
0
1100
0011
0
time
clock
registers
input
sequence of state change
clock
Figure 5-1
registers A, B, C, …
A=B+C

## Slide 4: What is RTL design
RTL: Register Transfer Level (Language)
a standard method to design any digital IC
Feature:
  designer specify rules to transfer data from one register to another register
  EDA (electronic design automation) tool synthesis RTL code to real hardware
reg [3:0] A, B, C;
always @(posedge clk) begin
A <= B+C;
end
Verilog code
+
B
C
A
clk
register

## Slide 5: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 6: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
Hey you, do A=B+C
A=B+C, where A, B, C are registers

## Slide 7: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
I got overflow from A=B+C, sir

## Slide 8: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 9: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 10: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 11: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 12: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)
K: A=B+C
(if (K==1) then A=B+C;)
K

## Slide 13: Now let’s talk about the dash watch
Example 6-3 of the textbook

## Slide 14: The Spec
start counting when “START” button pressed
  refresh every 0.01 second
  00.00 -> 00.01 -> 00.02 ->…00.99 -> 01.00 ->…
stop counting and holds current time when “STOP” button pressed
reset time to zero when “reset” button pressed
CSS: compare-and-store
  store the fastest value in internal storage
  e.g. 10.02 will replace 11.23
(Figure 6-25, Section 6-10)

## Slide 15: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 16: Step-by-step flow-chart for the dash watch
corresponding to a state-diagram for hardware implementation

## Slide 17: Registers/Counters we have
TM: time-value
  00:00 -> 00:01 -> 00:02 ->…
  the stopwatch of your lab
  4-digit BCD counter
SD: stored data
  the fastest time till now
  SD=(TM<SD)? TM: SD when “CSS” pressed
TM
SD

## Slide 18: Step-by-step flow-chart
a hardware algorithm represented as state-diagram

## Slide 19: Step-by-step flow-chart
a hardware algorithm represented as state-diagram
one step in one cycle

## Slide 20: Step-by-step flow-chart
a hardware algorithm represented as state-diagram
one-step micro-operation in one cycle

## Slide 21: Step-by-step flow-chart
Let’s trace the hardware algorithm

## Slide 22: Step-by-step flow-chart
the initial status
SD: Stored Data
  the internal storage for the fastest value
set SD=99.99 at initial

## Slide 23: Step-by-step flow-chart
Wait for start
TM: the Timing
  the register for the current value
set TM=00.00 until “START” pressed

## Slide 24: Step-by-step flow-chart
do counting after “START” pressed
time
state
control signals
TM
S3
do TM=TM+1
00.10
00.11
00.12
00.13
do TM=TM+1

## Slide 25: Step-by-step flow-chart
various decisions after “STOP” pressed

## Slide 26: Step-by-step flow-chart
various decisions after “STOP” pressed
wait until some button pressed

## Slide 27: Step-by-step flow-chart
various decisions after “STOP” pressed
restart counting if “START” pressed again

## Slide 28: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
compare and store
SD = min {TM, SD}

## Slide 29: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
if (TM<SD) SD=TM

## Slide 30: Step-by-step flow-chart
various decisions after “STOP” pressed
TM: current time value
SD: store data (fasted till now)
do nothing and hold SD if (TM >= SD)

## Slide 31: Step-by-step flow-chart
wait for the next “START”

## Slide 32: Step-by-step flow-chart
wait for the next “START”
re-start if “START” pressed again

## Slide 33: How to convert the “hardware algorithm” to real hardware?

## Slide 34: Mapping to RTL design framework

## Slide 35: Mapping to RTL design framework
micro-operations in data path side
we need registers TM and SD (16-bit for 4-digit time value)
TM
SD

## Slide 36: Mapping to RTL design framework
state-diagram realized in the control-unit side
use the standard method in Chap. 5

## Slide 37: Mapping to RTL design framework
control signals to inform which micro-operation to perform
TM
SD

## Slide 38: Mapping to RTL design framework
status signals to guide the state transition
TM
SD

## Slide 39: Mapping to RTL design framework
And, of course, lots of button inputs
TM
SD

## Slide 40: Now we are back to this RTL design flow
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 41: Behavior specification of the data path

## Slide 42: Registers in the datapath side
TM (time value): 16-bit counters
  composed of 4 BCD counters
  00:00 -> 00:01 ->… ->99:99
SD: (stored data) fasted time till now
  16-bit register with load enable control
TM
SD

## Slide 43: Registers in the datapath side
TM (time value): 16-bit counters
  composed of 4 BCD counters
  00:00 -> 00:01 ->… ->99:99
SD: (stored data) fasted time till now
  16-bit register with load enable control
TM
SD
SD = (TM<SD)? TM: SD;

## Slide 44: Micro-operations and control signals
RSTM, ENTM, UPDATE, LSR

## Slide 45: Micro-operations and control signals
operations on TM

## Slide 46: Micro-operations and control signals
operations on register SD

## Slide 47: Status signal back to control unit
ALTB: A LessThan B
ALTB

## Slide 48: Status signal back to control unit
SD = (TM<SD)? TM: SD;

## Slide 49: Micro-operations and control signals
all operations required by the “hardware algorithm” are defined by the micro-operations (check by yourself!)

## Slide 50: Behavior specification of the control unit
the state diagram

## Slide 51: Steps of RTL Design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 52: Behavior spec of the control unit
hardware algorithm
state diagram

## Slide 53: Behavior spec of the control unit
check for the match on the hardware algorithm!

## Slide 54: Behavior spec of the control unit
check for the match on the hardware algorithm!
LSR=1, UPDATE=0

## Slide 55: Behavior spec of the control unit
check for the match on the hardware algorithm!
ENTM=1

## Slide 56: Behavior spec of the control unit
check for remaining matches by yourself!

## Slide 57: Now we finish the behavior spec of the dash watch

## Slide 58: Circuit design from behavior spec

## Slide 59: Steps of RTL design
Step 0: write-down the “step-by-step” flow-chart for the task
Step 1: starts from the general framework
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 60: Control unit design
standard method from Chap. 4

## Slide 61: Control unit design
standard method from Chap. 4
do it yourself! (notice the timing!)
D flip-flops
combinational
circuit
LSR, RSTM,
ENTM, UPDATE,…
ALTB
START, STOP, RESET

## Slide 62: Data path design

## Slide 63: Data path design
two core registers
  TM (time value): 4-digit BCD counter
    00:00 -> 00:01 -> 00:02 ->…
  SD (stored data): 16-bit register with load enable

## Slide 64: Data path design
two core registers
  TM (time value): 4-digit BCD counter
  SD (stored data): 16-bit register with load enable

## Slide 65: Data path design
two core registers
  TM (time value): 4-digit BCD counter
  SD (stored data): 16-bit register with load enable
(Figure 6-2)

## Slide 66: Data path design
How to realize these micro-operations?

## Slide 67: Data path design
How to realize these micro-operations?
Very similar to your digital clock design!

## Slide 68: Data path design
How to realize these micro-operations?

## Slide 69: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 70: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 71: Data path design
How to realize these micro-operations?
  use multiplexer (MUX) to select between multiple inputs

## Slide 72: Data path design
realize by a combinational circuit to compare
  notice the timing!

## Slide 73: Data path design
And the part to control 7-seg display
  skipped due to our FPGA board has different configuration

## Slide 74: Put it all together

## Slide 75: The Spec
start counting when “START” button pressed
  refresh every 0.01 second
  00.00 -> 00.01 -> 00.02 ->…00.99 -> 01.00 ->…
stop counting and holds current time when “STOP” button pressed
reset time to zero when “reset” button pressed
CSS: compare-and-store
  store the fastest value in internal storage
  e.g. 10.02 will replace 11.23
(Figure 7-23, Section 7-10)

## Slide 76: (1) Step-by-step flow-chart
a hardware algorithm represented as state-diagram

## Slide 77: (2) Behavior specification

## Slide 78: (3) Circuit design

## Slide 79: Hard to imagine this circuit works, right?

## Slide 80: Do these exercises with your midterm project
Draw a “software flow-chart” for the hardware algorithm (as you learned in 計概)
Draw the timing diagram of your control unit (alone)
Draw the timing diagram of your data path (alone)
Put these two timing diagram together
  and back-trace how the “hardware algorithm” works
Put these diagrams into your midterm project report!